## Slide 1: Regular Meeting
Presenter: WEN YUHE wenyuhe@mail.ulsan.ac.kr Mar.05, 2026
1Dept. of Electrical, Electronic and Computer Engineering, University of Ulsan, Ulsan, Korea

## Slide 2: Last Last Week
Research
Goal : 4D Radar + Camera + IMU Fusion 3D Object Detection Model in Construction Field (jaeho, gan quan, yuhe)
Filtering
Key idea : Go-RIO, UA, IKF Erase ground & under ground points Calibrate vibration radar points by using gaussian process Imu(100hz) is faster than radar(15hz) Calibrate radar by one step ahead imu data
Clustering
Key idea : DDCFusion 3D lidar annotation is Ground Truth Radar & camera estimate 3D bbox Minimizing the loss through iterative training
Advance
Key idea : Tracking Sometime model miss object, but the object is still there. Object’s location & velocity doesn’t change rapidly Estimate object’s next position
original
radar
imu
filtered
radar
6DOF
Cluster
Points
(class+
Point info)
camera
6DOF
3D
BBOX
Object info

## Slide 3: Last Last Week
Research
Filtering noise, Vibration Calibration by using “Go-RIO + Uncertainty Aware + Iterated Kalman Filter”
Go-RIO : Using concentric zone to separate noise, Using GP to make 6DOF with asynchronized radar + imu
Uncertainty Aware : Propagates the GP posterior variance into per-point post-undistortion uncertainty (Σ_p) and performs motion- compensated point cloud undistortion
IKF : Estimates the state by assigning different weights to each point according to its post-undistortion uncertainty
Go-RIO
Fuses IMU and Radar Doppler via Gaussian Process to infer the sensor pose (position + orientation) and its uncertainty at any arbitrary time t
Uncertainty Aware
Converts the GP uncertainty output by Go-RIO into per-point positional uncertainty (Σ_p) and performs point cloud undistortion
IKF
Takes the undistorted points and their uncertainty (Σ_p), assigns higher weights to more reliable points, and estimates the final 6DOF state
original
radar
imu
filtered
radar
6DOF
GP
state+var
Filtered
Points
+
Σ_p
Σ_p : A 3×3 covariance matrix that represents how uncertain the 3D position of each point is after undistortion

## Slide 4: This Week
Research
Study
Gaussian Process
Uncertainty Aware
Kalman Filter & Iterated Kalman Filter
Develop
Make code of ROS2 Go-RIO(Gaussian Process)
Make Code of Uncertainty Aware Module
Meeting with gan quan, Jaeho

## Slide 5
Thank you